## Slide 1
wasp1 / RV32I + Zicsr / RISC-V Debug 0.13.x target
Debug Module
Design PPT
面向 OpenOCD/GDB 兼容目标的早期 Debug leaf 设计：DMI register file、halt/resume 控制、abstract GPR command、core GPR transport。
IF
JTAG DTM
future
IF
debug_dmi_if
req/rsp
SEQ
debug_dmi_regs
DM state
SEQ
core debug_if
halt/GPR
editable native PowerPoint shapes
1

## Slide 2
wasp1 / Debug Module
设计目标与边界
先做 OpenOCD/GDB 所需的最小可验证 Debug Module 骨架
- 符合 RISC-V External Debug Spec 0.13.x 的核心可见行为
- 单 hart，hart 0 有效；非零 hartsel 返回 nonexistent
- 支持 DM activation、halt/resume、havereset/resumeack 轮询
- 支持 RV32 GPR Access Register abstract command
- 所有状态使用 clk_i/rst_ni，IC / Virtex-7 / sim 行为一致
IF
DMI transport
ready/valid
SEQ
DM registers
state + response slot
SEQ
halt_ctrl
transaction FSM
SEQ
abstract_cmd
command FSM
SEQ
reg_access
GPR sequencer
2

## Slide 3
wasp1 / Debug Module
Debug leaf 总体结构
DMI register file 负责软件可见寄存器；控制器和 sequencer 负责可验证的时序语义
IF
Future JTAG DTM
scan / op / addr / data
IF
debug_dmi_if
modports
SEQ
debug_dmi_regs
dmcontrol/dmstatus
abstractcs/data0
SEQ
debug_halt_ctrl
halt/resume transaction
SEQ
debug_abstract_cmd
RV32 GPR command decode
SEQ
debug_reg_access
core GPR request/response
IF
core debug_if
halt/run
GPR
软件可见面
hart 控制面
GPR 数据面
3

## Slide 4
wasp1 / Debug Module
DMI register file 原理
一个 response slot 让 DMI backpressure 和同周期替换行为确定化
- 实现 6 个 DMI regs：data0、dmcontrol、dmstatus 等
- 未知地址或保留 op 返回 FAILED；只读写入成功但无副作用
- dmactive 清零会复位 DM 控制和 abstract 状态
- response slot 在空闲或本周期消费时接收新 request
- executor completion 独立于 DMI backpressure 更新 data0/cmderr
IF
DTM request
op/addr/data
COMB
op/address decode
read/write strobes
SEQ
response slot
valid/resp/data
clk_i/rst_ni
SEQ
dmcontrol regs
dmactive/hartsel
halt/resume/reset
SEQ
abstract regs
command/data0
cmderr W1C
COMB
read images mux
dmstatus/abstractcs
4

## Slide 5
wasp1 / Debug Module
dmcontrol / dmstatus 的根本逻辑
单 hart 系统里 any/all 状态成对相同；非零 hartsel 明确返回 nonexistent
寄存器
关键字段
设计理由
dmcontrol
dmactive, haltreq, resumereq, ndmreset, hartsel
调试器用一个寄存器完成激活、hart 选择和控制意图
dmstatus
version=2, authenticated=1, halted/running/resumeack/havereset
OpenOCD/GDB 轮询 hart 可用性与状态
abstractcs
busy, cmderr, datacount=1, progbufsize=0
把最小 GPR abstract command 的 busy/error 状态暴露给软件
command/data0
accepted command, one 32-bit data register
RV32 GPR 读写的数据通道
COMB
hartsel == 0
selected_hart_exists
COMB
hartsel != 0
any/all nonexistent
IF
hart status inputs
halted/running
resumeack/havereset
COMB
dmstatus image
any/all mirrors
version/auth fixed
5

## Slide 6
wasp1 / Debug Module
halt_ctrl：halt/resume 事务控制
把 DM 的 level intent 变成 core 可接收的 transaction，并保持 sticky software-visible 状态
- IDLE 只在需要时发起 HALT_WAIT 或 RESUME_WAIT
- halt 与 resume 同时出现时 halt 优先
- DM inactive、取消、core 完成或 hart reset 都会终止事务
- resumeack 和 havereset 做 sticky 保存，避免软件轮询漏掉短事件
IDLE
HALT_WAIT
RESUME_WAIT
IDLE -> HALT_WAIT: dmactive && haltreq && !core_halted
IDLE -> RESUME_WAIT: dmactive && !haltreq && resumereq && !core_running
WAIT -> IDLE: completion, cancel, dmactive clear, or reset event
6

## Slide 7
wasp1 / Debug Module
abstract_cmd：RV32 GPR Access Register
先做能被 OpenOCD/GDB 基础寄存器读写用上的最小 command executor 前级
- cmdtype=0 Access Register
- aarsize=2 when transfer=1
- regno=0x1000..0x101F
- transfer=0 is halted no-op
- write=1 writes data0 to GPR
IDLE
ISSUE
WAIT
COMPLETE
COMB
error mapping
NOTSUP
HALT_RESUME
EXCEPTION
关键原则：command capture 后请求字段保持稳定；读成功才 data0_we；DM deactivation 是 silent abort。
7

## Slide 8
wasp1 / Debug Module
reg_access：core GPR transport sequencer
不解码 abstract command，只保证一条 GPR 命令与 core response 精确配对
- cmd handshake 后锁存 write/address/wdata
- core request backpressure 下字段保持稳定
- same-cycle core response 可直接进入 LOCAL_RSP
- flush 后若 core 已接收请求，进入 DROP_RSP 消耗 stale response
- 每个非 flushed command 恰好产生一个 upstream response
IDLE
CORE_REQ
CORE_WAIT
LOCAL_RSP
DROP_RSP
DROP_RSP 不是错误态，而是 ownership barrier：防止旧 core response 被错误配给下一条命令。
8

## Slide 9
wasp1 / Debug Module
debug_dmi_if：只定义连接，不藏状态
interface 本身没有 storage、FSM、always_comb 或 always_ff
IF
dtm modport
request producer
response consumer
IF
debug_dmi_if
req_valid/ready
op/addr/data
rsp_valid/ready
resp/data
IF
dm modport
request consumer
response producer
- req channel: fields stable while req_valid && !req_ready
- rsp channel: fields stable while rsp_valid && !rsp_ready
- monitor modport is passive for assertions and scoreboards
- all buffering policy belongs to connected DTM/DM blocks
9

## Slide 10
wasp1 / Debug Module
验证方法：为什么这样测
每个 debug leaf 都用自检查 testbench 覆盖正常路径、边界、错误和 backpressure
目标风险
验证方法
根本逻辑
DMI backpressure
response hold + same-edge replace
DMI 是请求/响应分离协议，必须证明无气泡替换和稳定保持
halt/resume race
directed cancellation + random latency
core 状态变化不是固定延迟，事务控制必须对延迟不敏感
abstract command legality
unsupported field/error mapping sweep
调试器依赖 cmderr 精确区分 NOTSUP/HALT_RESUME/EXCEPTION
GPR response ownership
flush phase sweep + stale drain
取消后旧 response 不能污染下一条 command
target portability
generic/IC/Virtex-7 lint matrix
宏选择不能改变软件可见 Debug 行为
COMB
reference model
scoreboard
phase counters
IF
self-checking TB
directed + random
SEQ
PASS criteria
first mismatch fatal
coverage summary
10

## Slide 11
wasp1 / Debug Module
验证结果快照
当前报告是 functional self-check coverage；未声明 structural code/toggle coverage
模块
sim end
self-check
随机/关键覆盖
debug_dmi_regs
2116ns
74
16 random data0, response hold 67
debug_halt_ctrl
1056ns
102
8 random halt/resume pairs, held cycles 39
debug_reg_access
1866ns
181
20 random transactions, flush phases 4
debug_abstract_cmd
2066ns
202
20 random commands, unsupported classes 7
Generic lint PASS
IC lint PASS
Virtex-7 lint PASS
Functional sim PASS
所有 testbench 使用 1ns/1ps、10ns clock。覆盖重点是功能语义与协议持稳；后续集成阶段再加入端到端 OpenOCD/GDB 与结构覆盖。
11

## Slide 12
wasp1 / Debug Module
后续集成关注点
leaf 已验证，但完整 debug 链路还需要 JTAG DTM、core Debug Mode 和端到端调试器验证
SEQ
current verified leaves
dmi_regs
halt_ctrl
abstract_cmd
reg_access
COMB
integration work
JTAG DTM/TAP
core debug mode
debug ROM policy
IF
tool compatibility
OpenOCD probe
GDB register read/write
halt/resume session
- 把 Debug Module 接入 wasp1 顶层和 interrupt/core reset 策略
- 补齐 core-side dcsr/dpc/debug entry/exit 语义
- 建立 OpenOCD/GDB smoke + directed script 回归
- 在集成稳定后补 structural code/toggle coverage
12