## Slide 1
wasp1 / peripheral leaf / safety timer
Watchdog
Design PPT
AHB-Lite watchdog timer：timeout counter、kick key、clear priority、IRQ/reset request 输出，以及自检查验证。
IF
AHB-Lite slave
register access
SEQ
control/status
timeout/count
COMB
count+1 compare
timeout hit
IF
IRQ/reset request
SoC integration
editable native PowerPoint shapes
1

## Slide 2
wasp1 / AHB-Lite Watchdog Timer
设计目标与行为边界
软件定期写 KICK key；超时后 sticky status 驱动 IRQ 和 reset request
- AHB-Lite always-ready word register slave
- TIMEOUT=N 表示清零后 N 个 enabled ticks 到期
- TIMEOUT=0 作为 immediate expiry
- 正确 KICK 清 count/expired/reset_req；错误 key 只置 keyerr
- 模块自身不决定 SoC reset tree，只输出 wdg_reset_req_o
SEQ
CTRL regs
enable irq_en reset_en
SEQ
COUNT/TIMEOUT
up counter
SEQ
sticky status
expired reset_req keyerr
IF
wdg_irq_o
wdg_reset_req_o
2

## Slide 3
wasp1 / AHB-Lite Watchdog Timer
模块总体结构
AHB 请求锁存、寄存器状态、timeout compare 和输出 decode 明确分层
IF
AHB bus
hsel/haddr/htrans
hwrite/hsize/hwdata
COMB
address decode
range/alignment
word size
SEQ
request regs
clk=hclk_i
rst=hresetn_i
SEQ
control/status regs
timeout/count
expired/keyerr
COMB
count_plus_one
timeout_hit
TIMEOUT=0
COMB
read/status/output
HRDATA/HRESP
IRQ/reset_req
3

## Slide 4
wasp1 / AHB-Lite Watchdog Timer
软件寄存器模型
5 个 word registers 覆盖 enable、状态、timeout、count 和 feed 动作
Offset
Name
Access
Meaning
0x00
CTRL
RW
enable, irq_en, reset_en, clear
0x04
STATUS
RO
expired, reset_req, keyerr, running
0x08
TIMEOUT
RW
32-bit terminal count
0x0C
COUNT
RO
current watchdog count
0x10
KICK
WO
write WDG_KICK_VALUE to feed
IF
software flow
program TIMEOUT
set CTRL enable
periodic KICK
poll STATUS
COMB
KICK policy
correct key feeds
bad key latches keyerr
4

## Slide 5
wasp1 / AHB-Lite Watchdog Timer
更新优先级
clear/kick 必须能压过同周期 tick 或 expiry，这是 watchdog 语义最关键的地方
- reset 初始化全部寄存器和 AHB response
- 默认 watchdog tick 先计算 count_plus_one / timeout_hit
- 软件 CTRL.clear 或 valid KICK 在同一 always_ff 后部覆盖 tick
- bad KICK 不 feed，只 latch keyerr
- 未知寄存器和非法地址通过 HRESP ERROR 暴露
SEQ
reset
state init
COMB
tick/compare
count+1>=timeout
SEQ
software write
clear/kick/control
SEQ
final state
count/status/output
5

## Slide 6
wasp1 / AHB-Lite Watchdog Timer
Timeout / Kick 工作原理
count_plus_one 与 timeout_q 比较，避免 TIMEOUT=N 的 off-by-one 歧义
RUNNING
count<N
TIMEOUT_HIT
EXPIRED
sticky
KICK/CLEAR
count=0
TIMEOUT=0 直接命中；TIMEOUT=N 时从 count=0 开始，第 N 个 enabled tick 进入 expired。expired 后计数停止，直到 clear 或正确 KICK。
6

## Slide 7
wasp1 / AHB-Lite Watchdog Timer
STATUS、IRQ 与 reset request
expired 是 sticky completion；reset_req 只在 reset_en 到期时 sticky latch
Signal/bit
Definition
Why
STATUS.running
enable && !expired
软件可快速判断 watchdog 是否仍在计数
STATUS.expired
timeout hit latched
polling 和 IRQ 共享同一 completion source
STATUS.reset_req
reset_en sampled at expiry
reset 请求保持到 kick/clear
wdg_irq_o
expired && irq_en
IRQ mask 不改变 expired 状态
wdg_reset_req_o
reset_req_q
交给 SoC reset tree 处理
COMB
output decode
status image
IRQ/reset request
IF
SoC integration
interrupt input
reset controller
7

## Slide 8
wasp1 / AHB-Lite Watchdog Timer
AHB 响应与错误处理
always-ready 简化外设接入；非法访问仍在一拍后返回 HRESP ERROR
- hready_o 固定 1，不产生 wait state
- addr phase 捕获 req_valid/write/err/offset
- 只支持 aligned word access
- misaligned、non-word、out-of-range 返回 ERROR
- unknown register offset 在 data phase 返回 ERROR
IF
address phase
current bus
COMB
decode errors
range align size
SEQ
request regs
one-cycle delay
COMB
read/response
HRDATA/HRESP
8

## Slide 9
wasp1 / AHB-Lite Watchdog Timer
验证方法：为什么这样测
watchdog 的核心风险是计数边界、feed 优先级、sticky 输出和 AHB 错误契约
风险
验证方法
根本逻辑
reset/register contract
reset reads + register readback
软件只通过寄存器面配置和诊断
timeout boundary
timeout=4, reset-only, random timeout
证明 TIMEOUT=N 和 TIMEOUT=0 语义
feed priority
correct KICK before expiry
防止同周期 tick 错误抢先到期
bad key handling
wrong KICK value then STATUS read
错误 feed 不应隐藏软件 bug
AHB error path
misaligned/halfword/unknown/range
非法访问必须是总线错误而不是静默忽略
IF
self-checking TB
AHB driver
COMB
scoreboard
register/status
cycle timing
9

## Slide 10
wasp1 / AHB-Lite Watchdog Timer
验证结果快照
当前报告是 functional self-check coverage；generic/IC/Virtex-7 lint 与仿真均通过
Metric
Value
Meaning
pass_count
50
self-check milestones
reg_count
35
register access checks
timeout_count
2
directed timeout classes
kick_count
2
valid kick and pre-expiry feed
error_count
5
AHB / register error paths
random_count
4
deterministic random timeouts
Generic lint PASS
IC lint PASS
Virtex-7 lint PASS
tb_ahb_wdg PASS
Timebase: 1ns/1ps, 10ns verification clock. Cases cover reset, timeout IRQ/reset, valid/bad kick, clear behavior, IRQ masking, AHB error paths, and random timeout values.
10

## Slide 11
wasp1 / AHB-Lite Watchdog Timer
后续集成关注点
模块级 watchdog 已验证；reset request 如何进入 SoC reset tree 是顶层验证项
SEQ
current module
verified register file
timeout/kick logic
IRQ/reset outputs
COMB
integration work
reset tree policy
interrupt wiring
firmware driver
IF
system validation
end-to-end timeout
recovery behavior
boot interaction
- SoC 顶层要决定 wdg_reset_req_o 是局部复位还是全芯片复位
- 需要 firmware-driven kick/timeout 回归验证 reset/boot 交互
- 后续可补结构覆盖和长时间 soak/random timeout tests
11