## Slide 1
wasp1 / peripheral leaf / AHB-Lite slave
I2C Master
Design PPT
最小 single-master I2C 控制器：AHB 寄存器、byte FSM、prescale divider、open-drain SCL/SDA drive enables，以及自检查验证。
IF
AHB-Lite slave
register access
SEQ
software regs
DATA/STATUS/CTRL
SEQ
I2C byte FSM
START/BIT/ACK/STOP
COMB
open-drain decode
SCL/SDA OE only
editable native PowerPoint shapes
1

## Slide 2
wasp1 / AHB-Lite I2C Master
设计目标与非目标
把 I2C 做成可验证、可综合、对软件清晰的最小主控外设
- single-master，一次 CMD 写启动一个 8-bit byte transaction
- AHB-Lite always-ready slave，地址相位后一拍返回 data/response
- 软件配置 START/READ/STOP/ACK_VALUE，DATA 承载 TX/RX byte
- SCL/SDA 只提供低电平 drive enable，高电平由外部 pull-up
- 不实现 multi-master arbitration、clock stretching 和 pad 签核
IF
software-visible
AHB registers
SEQ
byte FSM
one byte per CMD
COMB
open-drain policy
OE means drive low
IF
external pull-ups
board/pad domain
2

## Slide 3
wasp1 / AHB-Lite I2C Master
模块总体结构
AHB 寄存器面和 I2C bit/ACK/STOP 时序面分离，组合 open-drain decode 输出到 pad
IF
AHB bus
hsel/haddr/htrans
hwrite/hsize/hwdata
COMB
address decode
range/alignment
known offset
SEQ
request phase regs
clk=hclk_i
rst=hresetn_i
SEQ
software regs
enable irq prescale
tx/rx/status/cmd
SEQ
I2C byte FSM
START BIT ACK STOP
divider tick
COMB
read/status/output
HRDATA/HRESP
IRQ
SCL/SDA OE
software register plane
serial timing plane
3

## Slide 4
wasp1 / AHB-Lite I2C Master
软件寄存器与命令模型
寄存器面足够小：DATA/STATUS/CTRL/PRESCALE/CMD 覆盖一个 byte transaction
Offset
Name
Access
Meaning
0x00
DATA
RW/RO
write TX byte; read last RX byte
0x04
STATUS
RO
busy, done, ackerr, rx_valid, irq
0x08
CTRL
RW
enable, irq_en, write-one clear
0x0C
PRESCALE
RW
16-bit phase divider reload
0x10
CMD
WO
START, READ, STOP, ACK_VALUE
COMB
CMD bits
START bit0
READ bit1
STOP bit2
ACK_VALUE bit3
IF
software flow
program DATA/PRESCALE
write CTRL enable
write CMD
poll STATUS/read DATA
4

## Slide 5
wasp1 / AHB-Lite I2C Master
AHB-Lite 响应原理
always-ready 简化互连；地址相位 metadata 锁存到下一拍 response/data phase
- hready_o 固定为 1，模块不向 AHB 插入等待周期
- addr phase 检查 hsel、htrans[1]、range、alignment、word size
- req_valid_q/req_write_q/req_err_q/req_offset_q 保存一拍
- read_data_next 由已锁存 offset 和当前寄存器状态组合产生
- 未知 offset、非法 size、busy/disabled CMD 返回 HRESP ERROR
IF
AHB address phase
current bus pins
COMB
decode
range/align/size
SEQ
request regs
one-cycle delay
COMB
response mux
HRDATA/HRESP
5

## Slide 6
wasp1 / AHB-Lite I2C Master
I2C byte FSM
一个 CMD 只执行一个 byte；START/STOP 是否出现由 CMD 位控制
IDLE
START_A
START_B
BIT_LOW
BIT_HIGH
ACK_LOW
ACK_HIGH
STOP_LOW
STOP_HIGH
DONE
BIT_LOW/BIT_HIGH 循环 8 次，由 bit_idx_q 从 7 数到 0。TX 在 ACK_HIGH 采样 slave ACK；RX 在 BIT_HIGH 采样数据，并在 ACK_HIGH commit RX byte。
6

## Slide 7
wasp1 / AHB-Lite I2C Master
PRESCALE divider 与 tick
I2C 时序推进由 phase tick 驱动；PRESCALE=0 合法，便于快速仿真
- prescale_q 是 16-bit reload value
- FSM active 时 div_q 递减；div_q==0 产生 tick
- tick 后 div_q 重新装载 prescale_q
- FSM idle 时 div_q 跟随 prescale_q
- PRESCALE=0 表示每个 hclk_i cycle 推进一个 FSM phase
SEQ
prescale_q
software reload
SEQ
div_q counter
clk=hclk_i
COMB
tick = div_q==0
phase enable
SEQ
byte FSM
advance on tick
7

## Slide 8
wasp1 / AHB-Lite I2C Master
Open-drain SCL/SDA 策略
模块永远不驱动逻辑 1；输出值固定为 0，OE 决定是否把线拉低
- i2c_scl_o = 0，i2c_sda_o = 0
- *_oe_o = 1 表示 drive low；*_oe_o = 0 表示 release
- TX bit 为 0 时 SDA OE=1；TX bit 为 1 时 release
- RX data phase 释放 SDA，由外部 slave 驱动
- RX ACK: ACK_VALUE=0 拉低 ACK，ACK_VALUE=1 释放为 NACK
SEQ
FSM state
cmd direction
bit_idx/tx bit
COMB
line decode
SCL_OE/SDA_OE
IF
external line
pull-up + pad
SCL/SDA observed
drive low only
8

## Slide 9
wasp1 / AHB-Lite I2C Master
状态、IRQ 与错误处理
错误响应保护软件模型；done/ackerr/rx_valid 构成一次 transaction 的 completion contract
Item
Set condition
Clear condition
done
FSM reaches DONE
CTRL.clear or new CMD
ackerr
TX ACK_HIGH samples SDA high
CTRL.clear or new CMD
rx_valid
RX ACK_HIGH commits byte
CTRL.clear or new CMD
irq
done && irq_en
done cleared or irq_en=0
COMB
error detect
misaligned
non-word
unknown offset
CMD disabled/busy
IF
AHB response
HRESP ERROR
no restart/corrupt
9

## Slide 10
wasp1 / AHB-Lite I2C Master
验证方法：为什么这样测
I2C 外设的风险集中在寄存器契约、串行线行为、busy 保护和错误响应
风险
验证方法
根本逻辑
register contract
reset + legal read/write sweep
软件只能通过寄存器面观察和控制 byte engine
AHB error response
misaligned/byte/unknown/out-of-range
总线错误必须在一拍响应中准确暴露
TX bit drive
0xA5, 0x3C, random TX + line checks
最终 done 不足以证明 open-drain bit-level 正确
RX sampling/ACK
feed 0x5A/0xC3; ACK and NACK cases
读方向同时验证 sample timing 和 master ACK policy
busy protection
issue CMD while FSM active
第二条命令不能重启或破坏当前 transaction
IF
self-checking TB
AHB driver
I2C slave model
COMB
scoreboard
register image
line-level checks
10

## Slide 11
wasp1 / AHB-Lite I2C Master
验证结果快照
当前报告是 functional self-check coverage；目标宏 lint 和仿真均通过
Metric
Value
Meaning
pass_count
110
self-check milestones
reg_count
36
register access checks
write_tx_count
6
TX byte transactions
read_rx_count
2
RX byte transactions
error_count
5
AHB / command error cases
random_count
4
deterministic random TX bytes
line_check_count
50
open-drain bit-level checks
Generic lint PASS
IC lint PASS
Virtex-7 lint PASS
tb_ahb_i2c PASS
Timebase: 1ns/1ps, 10ns verification clock. Directed cases cover reset, legal/illegal AHB access, TX ACK/NACK, RX ACK/NACK, busy reject, and four deterministic-random TX bytes.
11

## Slide 12
wasp1 / AHB-Lite I2C Master
后续集成关注点
当前模块满足 wasp1 最小 I2C master contract，系统级仍要验证 pad 与外部设备时序
SEQ
current module
verified AHB slave
byte FSM
open-drain OE
COMB
integration work
pad wrapper
pull-up choice
board timing
IF
system validation
real I2C target
firmware driver
IRQ path
- multi-master arbitration 和 clock stretching 仍是明确非目标
- FPGA/IC pad open-drain 实现需要在顶层 wrapper 中确认
- 系统集成后增加 firmware-driven I2C peripheral 回归
- 后续可补结构覆盖和外设 timing margin signoff
12