## Slide 1
wasp1 / RV32I+Zicsr / AHB-Lite 2M x 10S
wasp1 SoC
Top Design PPT
单核 SoC 集成顶层：tile、cache、core AHB bridge、2-master fabric、OTP/SRAM/peripherals、IRQ pack、debug boundary 和 smoke verification。
SEQ
tile
RV32I+Zicsr
I/D cache
SEQ
AHB fabric
core + DMA masters
SEQ
OTP/SRAM/peripherals
10 slave windows
IF
UART/I2C/GPIO
debug/trap/reset pins
editable native PowerPoint shapes
1

## Slide 2
wasp1 / SoC Integration Top
顶层设计目标与边界
顶层负责结构集成和边界暴露，不重新实现子模块内部功能
- boot_pc 固定为 OTP_BASE，使 OTP 成为 reset 后可执行程序存储
- 把 tile I-cache/D-cache downstream 合并为 core-side AHB master
- 集成 DMA 第二 master 和 10 个 decoded external slave windows
- 打包 WDG/UART/I2C/GPIO/DMA 到 INTC，timer 直连 MTIP
- 临时暴露 core debug discrete ports；完整 JTAG DTM/DM 是后续集成项
SEQ
tile owns CPU/cache state
COMB
top owns wiring
IRQ pack
bridge select
SEQ
bridge owns
transaction state
IF
external pins
IO/debug/observe
2

## Slide 3
wasp1 / SoC Integration Top
2M x 10S AHB-Lite 拓扑
M0 来自 core-side bridge，M1 来自 DMA；fabric 负责仲裁、decode、mux 和 default response
IF
M0 core bridge
I/D cache traffic
SEQ
M1 DMA master
copy engine traffic
SEQ
ahb_fabric_2m
arbiter + default
registered response
COMB
decoder/mux
slave select
response mux
SEQ
10 slave windows
OTP ISRAM DSRAM DMA
WDG TIMER INTC
UART I2C GPIO
grant observation: bus_grant_idx_o
3

## Slide 4
wasp1 / SoC Integration Top
外部 slave windows
wasp1 顶层使用 common package 的 base address 和 slave index，保持全 SoC 一致
Group
Windows
Role
Program/storage
OTP, I-SRAM, D-SRAM
boot code and scratch memories
DMA
DMA control window
software controls second AHB master
System
WDG, TIMER, INTC
reset request, MTIP, MEIP aggregation
Serial/IO
UART, I2C, GPIO
external communication and pins
SEQ
boot path
boot_pc=OTP_BASE
tile fetch -> bridge
-> fabric -> OTP
COMB
data path
loads/stores/DMA
decode to SRAM or peripherals
4

## Slide 5
wasp1 / SoC Integration Top
Core I/D to AHB bridge
bridge 把 tile 的 imem_if/dmem_if 合并为一个 core-side AHB master，D-cache idle 仲裁优先
- BR_IDLE 中 dmem valid 优先于 imem valid
- BR_ADDR 驱动 AHB address phase，等待 hready
- BR_RESP 采样 hrdata/hresp，进入 response hold
- BR_RSP_HOLD 保持 cache response 直到 selected port ready
- 当前设计只允许 one outstanding single-beat transfer
BR_IDLE
BR_ADDR
BR_RESP
BR_RSP_HOLD
D-cache wins when both request
5

## Slide 6
wasp1 / SoC Integration Top
Reset 与 boot fetch flow
reset 后 tile boot PC 指向 OTP_BASE；第一条取指路径验证 SoC memory path 是否贯通
IF
hclk_i/hresetn_i
SoC reset domain
SEQ
tile/frontend
boot_pc=OTP_BASE
SEQ
core AHB bridge
imem request
SEQ
AHB fabric
M0 grant/decode
SEQ
executable OTP
AHB_SLAVE_OTP
当前顶层 smoke test 观察 core-side bridge/fabric path 是否出现 valid transfer；完整软件 boot、OTP 编程和 LLVM 输出执行仍是后续系统验证。
6

## Slide 7
wasp1 / SoC Integration Top
Interrupt integration
timer 直接作为 MTIP；外设 IRQ 通过 INTC 聚合为 MEIP，source 0 保留
INTC source
Signal
Origin
1
wdg_irq
Watchdog timeout
2
uart_irq
UART RX/TX/events
3
i2c_irq
I2C transaction done
4
gpio_irq
GPIO edge/level
5
dma_irq
DMA done/error
COMB
irq_src pack
{dma,gpio,i2c,uart,wdg,0}
SEQ
ahb_intc
mask/pending/claim
meip_o
SEQ
tile/core CSR
external_irq_i
timer_irq_i
SEQ
timer_irq
direct MTIP
7

## Slide 8
wasp1 / SoC Integration Top
IO 与 debug boundary
顶层暴露真实 IO pins，同时保留临时 discrete core debug channel 便于后续 DM/JTAG 接入
- UART RX/TX、I2C open-drain SCL/SDA value/OE、GPIO in/out/OE
- wdg_reset_req_o 暴露给后续 SoC reset tree
- trap_valid/cause 和 bus_grant_idx 用于 bring-up observation
- 内部实例化 debug_if，映射到 discrete top ports
- 完整 DMI/DTM/OpenOCD/GDB 兼容路径仍是 debug/wasp1 后续集成项
IF
external pins
UART/I2C/GPIO
WDG reset/trap/bus
IF
temporary debug ports
halt/resume/step
GPR req/rsp
SEQ
core_debug interface
inside tile/core
8

## Slide 9
wasp1 / SoC Integration Top
Target support 与模块责任边界
顶层不引入 target-specific 行为；target 宏由 child memory/wrapper/attribute 层消化
- WASP1_TARGET_SIM_GENERIC：通用仿真路径
- WASP1_TARGET_IC：IC synthesis macro path
- WASP1_TARGET_FPGA_XILINX_VIRTEX7：Xilinx Virtex-7 macro path
- 顶层保持 programmer-visible behavior、AHB、IRQ、debug boundary 一致
- memory wrappers 和目标属性由子模块负责
SIM_GENERIC lint PASS
IC lint PASS
Virtex-7 lint PASS
COMB
same software-visible
SoC contract
9

## Slide 10
wasp1 / SoC Integration Top
顶层验证方法：为什么这样测
顶层 smoke test 不重复 leaf coverage，而是证明集成 elaboration、reset 和第一条 fetch path
风险
验证方法
根本逻辑
full hierarchy integration
generic/IC/Virtex-7 lint
证明 54 integrated modules 可展开且 target 宏一致
reset IO safety
4 cycles reset + output checks
顶层 IO 不能在 reset 后产生危险驱动
first fetch path
wait core AHB valid transfer
OTP boot path 必须穿过 tile/bridge/fabric
debug status wiring
wait running or halted
debug_if discrete ports 已被驱动而非悬空
idle peripheral stability
extra cycles check WDG/I2C benign
未编程外设不能产生 reset 或 open-drain drive
IF
tb_wasp1
reset/observe
no firmware yet
COMB
integration smoke
pass counter
status snapshot
10

## Slide 11
wasp1 / SoC Integration Top
验证结果快照
当前报告是 integration smoke test；完整系统软件验证仍在后续
Check
Result
Evidence
Generic lint
PASS
make -C wasp1 lint
IC-target lint
PASS
make -C wasp1 lint-ic
Virtex-7 lint
PASS
make -C wasp1 lint-fpga-v7
tb_wasp1 simulation
PASS
pass_count=5
Observed debug
driven
dbg_running=1 dbg_halted=0
trap_valid=0
trap_cause=0x02
bus_grant_idx=0
WDG/I2C idle benign
Simulation window: reset to 276ns. The test confirms benign reset defaults, first core-side AHB activity, and driven debug status; it does not claim full boot/software coverage.
11

## Slide 12
wasp1 / SoC Integration Top
后续集成关注点
顶层结构已经可 elaboration/smoke，但完整 wasp1 产品化还需要系统软件和 debug/JTAG 闭环
SEQ
current top
structural SoC
OTP fetch smoke
IO/debug boundary
COMB
integration work
Debug Module/JTAG
OTP programming flow
DMA real memory copy
IF
system validation
OpenOCD/GDB
firmware boot
interrupt-driven tests
- 把 debug leaf/DM/JTAG DTM 接入 wasp1 顶层，实现 OpenOCD/GDB end-to-end
- 建立 OTP 用户程序装载、LLVM/BSP 输出、真实 boot regression
- 补 DMA through-memory copy、interrupt-driven firmware、timer/INTC 外设联动
- 后续增加结构 coverage、长时间 SoC random/soak 和 FPGA bring-up checklist
12